## Slide 1: Preliminary Results
Accounting for Uncertainty with Neural Nets
04.05.2018

## Slide 2: Contents
Multi-Objective Program (MOP)
Robust Formulation
  Solution Evaluation
  Recourse vs No Recourse
Scenario Generation with Distribution

## Slide 3: Multi-Objective Program (MOP)
First find optimal oil production level by solving
Then produce Pareto front by minimizing gas variance while keeping oil production above level α:

## Slide 4: MOP – Pareto Front
Y-axis is «Precision», the difference between maximum variance and variance given α
Use this measure to get desired shape where «right upwards» represents better solutions
Plot on the right: Pareto front for α ϵ [0.01, 1]
Chart: Pareto Front

## Slide 5: MOP – Discussion Points
How do we treat individual standard deviations/variance of 7 wells in a single optimization problem?
Independent wells mean variance should cancel out on aggregate (with many wells)
Difficult to quantify covariance
May still be reasonable to consider sum as «total uncertainty»?

## Slide 6: Robust Formulation
Ensure gas capacity constraint holds in all scenarios:
Scenarios generated by drawing variance factor per well per scenario:

## Slide 7: Scenario Evaluation
Two ways to evaluate scenarios:
  No recourse, infeasibility occurs
  Recourse, avoid infeasibility
Generally solve problem for ≤ 100 scenarios and evaluate for ≥10 000 scenarios

## Slide 8: Results, No Recourse
Follow choke values from solution regardless of whether we hit infeasibility
As expected, EEV yields infeasible values in about 49,7% of the scenarios (red bars top histogram)
100 scenarios solution is infeasible in about 3,8% of the scenarios (red bars bottom histogram)
If we record oil output in infeasible scenarios as 0, this evaluation will be very strict w.r.t the EEV solution

## Slide 9: Results, Recourse Option
Recourse heuristic:
  For each scenario, sequentially turn on well choke settings until we hit the gas capacity constraint
  We then stop and record objective solution
Order of wells to turn on decided by their mean gas-oil-ratio (GOR) over all feasible choke settings, where wells with low GOR are turned on first
More realistic evaluation of scenarios

## Slide 10: Results, Recourse Option
The robust solution is only infeasible in 3,8% of the scenarios and follows the heuristic in these cases
The robust solution with recourse reaches average oil output of 110

## Slide 11: Results, Recourse Option
Since EEV produces a solution that is infeasible in 50% of the scenarios, it is «rewarded» by being allowed to follow the greedy heuristic in these scenarios
EEV with recourse thus reaches an average oil output of 117
In 50% of scenarios, EEV is a wait-and-see heuristic

## Slide 12: Scenario Generation with Distribution
Create scenarios by sampling from one of the distributions given by the neural network:
µOFF
Var[yi]
Then fit a new neural network to the sampled points
Since variance is «baked into» sample, scenario network is just output predictions without variance

## Slide 13: Scenario Generation with Distribution